## Slide 1
Neural Network Image Detection for SmartSSD Platform
Jackson Hafele, William Zogg
CPR E 563 Final Report Spring 2023
Notes: William
1

## Slide 2
Motivation
Image detection is a notoriously high-BW ML application. [1]
Computational Storage Devices (CSD) bring ML acceleration closer to the necessary storage. [2]
Smart SSD can be an all-in-one solution combining:
  Large, fast flash storage to store an entire neural network.
  Close, customizable FPGA acceleration to utilize high BW.
[3]
Notes: William

## Slide 3
Background - Neural Network Application
Image classification using the TinyImageNet dataset
Utilizes 12 layer neural network to classify an image into 1 of 200 classes
Each layer is computationally heavy.
Thousands of data values loaded for every single inference
[7]
[8]
Notes: Will

## Slide 4
Background - Convolution Process
Evaluate strength of a filter to identify features in images
Higher number -> Higher presence of filter
Data Used:
  Input Data (3D array)
  Filter Data (4D array)
  Output Data (3D array)
[9]
Notes: Will

## Slide 5
Background - SmartSSD
3.84 TB NAND Flash Samsung SSD [4]
  NVMe Connection
AMD Kintex Ultrascale+ FPGA
  Utilize Vitis to synthesize C
  Reconfigurable
PCIe Switch between SSD, FPGA, and Host CPU
SmartSSD Architecture [5]
Notes: Jake

## Slide 6
Related Works - SmartSSD Accelerator
Common CPUs unable to utilize high bandwidth with multiple SSDs
Solution proposes to use SmartSSD for faster computations
Evaluates SparkSQL framework with TPC-H (benchmark)
Compare acceleration between CPU, external FPGA (Alveo U250) and SmartSSD [5]
Compares multiple results:
  Execution Time Speedup
  Performance Per Watt
  CPU Utilization
Notes: Jake

## Slide 7
Related Works - SmartSSD Accelerator
External FPGA and SmartSSD Speedup Results [5]
Analyzes Speedup between baseline CPU, Alveo U250 accelerator cards, and SmartSSD
Analyzes with multiple SSDs
Large improvement with throughput of SmartSSD
Notes: Jake

## Slide 8
Related Works - NeSSA
Data movement can take as much as 80% of total time for warehouse-scale operations
Proposes near-storage acceleration model involving SmartSSD to reduce data movement
Select subsets of large datasets to train while maintaining accuracy
  Uses multiple datasets to train model (includeTinyImageNet)
Analyzes accuracy of NeSSA training and time to train
  Compares multiple subset sizes with other training models [6]
Notes: Jake

## Slide 9
Related Works - NeSSA
Percent of time Training Neural Networks Vs. Data Movement Latency for Machine Learning Models[6]
Authors compare time spent on computation and data movement for multiple models
Demonstrates importance of improving Data Movement latency for future works
Notes: Jake

## Slide 10
Solution Approach
Run Neural Network application on Host Machine
  Utilize existing CPRE487/587X library, gain baseline results
Convolution Kernel Synthesis
  Refactor Convolution Layer to individual function
  Synthesize Kernel in Vitis
Run Neural Network application on SmartSSD application
  Compile with Vitis
  Peer to Peer communication between SSD and FPGA
Optimize Kernel design and memory transactions to reduce latency
Notes: Will

## Slide 11
Host Process
Host Code Steps
Read Convolution inputs from SSD to Host
Compute Floating Point operations on Host CPU
Write resulting convolution output from Host to SSD
Datapath
Control
Step 3
Step 1
Step 2
Notes: William

## Slide 12
SmartSSD Process
Host Code Steps
Initialize Kernel and SmartSSD
Write convolution inputs from Host to SSD in fixed blocks
Read input arguments from SSD to FPGA
Activate Kernel
Write output from FPGA to SSD
Read value from SSD to Host to Verify
Step 1
Step 2
Step 6
Step 3
Step 3
Step 3
Step 5
Step 5
Step 5
Step 4
Step 4
Datapath
Control
Notes: William

## Slide 13
Neural Network with Host
Run baseline code on SmartSSD device WITHOUT FPGA
Majority of time spent on data movement
  Reading takes majority of time: 0.459 seconds
  Writing data has minimal overhead: 0.002 seconds
Computing FP operations takes 0.195 seconds
A single inference for a low-res test image takes 0.672 seconds
How can we reduce data movement with SmartSSD?
Notes: Will

## Slide 14
Convolution Kernel
Created separate class for Layer 2 Convolution
  Enabled changes to Layer 2 while keeping rest of code same
  Convolve operation moved to independent function
  Called within the 3 level nested for loop
Created function for single point convolution
  Flattened 3D and 4D arrays into 1D arrays for synthesis and interfacing
  800 loop iterations to operate in kernel per call
Notes: Jake

## Slide 15
Convolution Kernel
Layer 2 Convolution Function
Notes: Jake

## Slide 16
Convolution Kernel
Single Point Convolution Function, Target Kernel
Notes: Jake

## Slide 17
SmartSSD Application
Created Host code for Peer to Peer memory transactions between Host/SSD and SSD/FPGA
Synthesized Kernel code to run on SmartSSD FPGA
Verified expected kernel output of convolution point
Collected timing metrics with chrono C++ library
  Inconsistent results for individual read/compute/write operations
SmartSSD Architecture [5]
Notes: Jake

## Slide 18
SmartSSD Optimization
Problem
  Latency of FPGA kernel extremely slow
  Memory transactions limited by 512 Byte minimum read/write size
  Read/Write transactions not utilizing high bandwidth
Solution
  Reduce amount of empty data read/write due to minimum block size to increase data bandwidth
  Reduce Kernel latency by adding parallelization of single point
  Compute multiple points in 1 kernel call to increase data bandwidth
    Less read/write transaction overhead from host
Notes: William

## Slide 19
SmartSSD Optimization
Kernel Improvements
  Old Kernel: 9107 cycles for 1 point
  Final Kernel: 708,747 cycles for 1024 points, average 692 cycles for 1 point
    Computes 1024 points per kernel call, loop unrolling with stride 32
    Average 0.865 cycles per loop iteration with parallelization
Read Improvements
  Old Host: Reads 4096 Values per point, Only 1602 Used
  Final Host: Reads 1600 Values per point, Fully utilized
Write Improvements
  Old Host: Writes 1024 Values per point, only 1 Used
  Final Host: Writes 1 value per point, Fully utilized
Notes: William

## Slide 20
Results
Full Layer Baseline CPU: 0.662 seconds
Original SmartSSD: 32.246 seconds
48x SPEED DOWN
Large improvement when running multiple convolution operations in one kernel
Majority of time spent reading data from SSD and computing kernel
Notes: William

## Slide 21
Results
Full Layer Baseline CPU: 0.662 seconds
1024 Points per Kernel: 0.4778 seconds
1.38x SPEED UP
More points per call ->
  less latency overhead from kernel call control
  Higher data bandwidth in read transactions
Notes: William

## Slide 22
Results
Speedup normalized to Baseline CPU
Data read from SSD: 1.74X SPEED UP
Kernel computations still slightly slower than baseline, room for improvement with Vitis HLS
Data writes slower, due to low bandwidth transaction of 1 block writeback per 1024 points
Notes: William

## Slide 23
Results
Baseline CPU: 70.50% moving data
1024 Point: 53.82% moving data
As data bandwidth increases per N point operations, % data movement decreases
Final design also has lower data movement latency
Leaves more room for improvement in optimizing kernel or write transactions
Notes: William

## Slide 24
Analysis
Application specific designs will take tailoring to achieve performance benefits, as seen with original FPGA design
SmartSSD can provide speedup in terms of overall execution time while lowering the gap between data movement and computation time
Designs benefit from high bandwidth applications and parallelization of FPGA design
Notes: William

## Slide 25
Future Work
Potential improvement for computation time of floating point operations in FPGA kernel
  More parallelization, compute 1024 points faster
Could speed up writeback by increasing write bandwidth larger than 1 4KB block
  Store full layer of points then write back with one write transaction
Notes: William

## Slide 26
References
[1] J. Do, V. C. Ferreira, H. Bobarshad, M. Torabzadehkashi, S. Rezaei, A. Heydarigorji, D. Souza, B. F. Goldstein, L. Santiago, M. S. Kim, P. M. V. Lima, F. M. G. França, and V. Alves, “Cost-effective, energy-efficient, and scalable storage computing for large-scale ai applications,” ACM Trans. Storage, vol. 16, oct 2020.
[2] D. Fakhry, M. Abdelsalam, M. W. El-Kharashi, and M. Safar, “A review on computational storage devices and near memory computing for high performance applications,” Memories - Materials, Devices, Circuits and Systems, vol. 4, p. 100051, 2023.
[3] https://miro.medium.com/max/700/1*oB3S5yHHhvougJkPXuc8og.gif
[4] https://www.xilinx.com/applications/data-center/computational-storage/smartssd.html
[5] J. H. Lee, H. Zhang, V. Lagrange, P. Krishnamoorthy, X. Zhao and Y. S. Ki, "SmartSSD: FPGA Accelerated Near-Storage Data Analytics on SSD," in IEEE Computer Architecture Letters, vol. 19, no. 2, pp. 110-113, 1 July-Dec. 2020, doi: 10.1109/LCA.2020.3009347. keywords: {Field programmable gate arrays;Bandwidth;Random access memory;IP networks;Pipelines;Data analysis;Throughput;SmartSSD;data analytics;spark;parquet;SSD}
[6] Neha Prakriya, Yu Yang, Baharan Mirzasoleiman, Cho-Jui Hsieh, and Jason Cong. 2023. NeSSA: Near-Storage Data Selection for Accelerated Machine Learning Training. In Proceedings of the 15th ACM Workshop on Hot Topics in Storage and File Systems (HotStorage '23). Association for Computing Machinery, New York, NY, USA, 8–15. https://doi.org/10.1145/3599691.3603404
[7] https://miro.medium.com/v2/resize:fit:1200/1*QnKckNSZilG3HxytJZUoAw.png
[8] https://assets-global.website-files.com/5d7b77b063a9066d83e1209c/627d1225cb1b3d197840427a_60f040a887535b932a3b2b6e_cnn-hero%2520(1).png
[9] https://assets-global.website-files.com/614c82ed388d53640613982e/646371e3bdc5ca90dee5331b_convolutional-neural-network%20(1).webp

## Slide 27
Questions

## Slide 28
Supplemental

## Slide 29
Supplemental

## Slide 30
Supplemental

## Slide 31
Supplemental

## Slide 32
Supplemental

## Slide 33
Supplemental
Final Kernel Latency Delays
Original Kernel Latency Delays

## Slide 34
Supplemental
Final Kernel Utilization

## Slide 35
Supplemental
Final Kernel Code

## Slide 36
Supplemental
Write to SSD From Host
Read from SSD to Host

## Slide 37
Supplemental
Read from SSD to FPGA
4. Write to SSD from FPGA
2. Set Input Arguments for Kernel to buffer pointers
3. Call FPGA Kernel